## Slide 1: Unified IPv6 Transition Framework With Flow-based Forwarding
draft-cui-softwire-unified-v6-framework-00 (was draft-cui-intarea-unified-v6-framework-01)

## Slide 2: Motivation
There has been many softwire transition mechanisms
  Lightweight 4over6, MAP-E etc.
Difficulty on addressing / provisioning
  MAP: Algorithmic mapping between IPv4/IPv6 addressing
  Lw4over6: Needs dynamic binding between IPv4/IPv6 addresses
More flexible and cost effective by applying softwire defined networking
  Easy to change network behavior
  Same forwarding device for all mechanisms

## Slide 3: Introduction
Design a unified framework for IPv6 transition
  Support IPv4 over IPv6 tunneling scenario
  Reduce unnecessary configuration/operations in current mechanisms
Based on SDN
  Replace routers (CPE/BR/AFTR) with OpenFlow switches
  Use centralized controller to define network behavior, and manage devices

## Slide 4: Architecture
CPE Switch
BR Switch
ISP IPv6 Network
Customer Network
Internet
Controller
OpenFlow Switch
Replace MAP CE, lwB4, …
As customer network gateway
OpenFlow Switch
Replace MAP BR, lwAFTR, …
  OpenFlow Controller
  Manage CPE/BR Switches: IP addressing, forwarding states, etc.
  May combined with DHCPv6 server

## Slide 5: Switch Configuration
Device configuration
  Initially, each CPE Switch is configured with:
    An IPv6 address/prefix Connect to controller through IPv6
    Controller’s IPv6 address
  Automatic address configuration for CPE: recommend DHCPv6
Forwarding configuration
  Use Openflow for configuring Switches’ forwarding rules
  Rule format: Match - Action
  Softwire information can be embedded into a rule, no provisioning needed
    E.g. BR Address: Destination address of CPE’s tunnel encapsulation action IPv4 address and PSID: Matching conditions of BR’s downstreaming rules, or values of set-field actions (to implement NAT44)

## Slide 6: Requirements for Switches
On top of OpenFlow switch
Action:
  Both CPE&BR: Support IPv6 tunneling action
Match:
  BR Switch: Support match field masking for ports (For MAP/lw4o6) => Reduce number of rules, BR Switch treat all traffic to the same IPv4 address + port set as a single flow

## Slide 7: Example: lw4over6 1. CPE Device Configuration
CPE Switch requests an IPv6 address (or prefix), and builds OpenFlow connection
Controller allocates an available IPv4 address + PSID for the CPE in local binding table
CPE Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
allocate 2001::1 through DHCPv6
OpenFlow connection
lw4over6 binding table

## Slide 8: Example: lw4over6 2. BR Forwarding Configuration
For every binding state: Controller installs forwarding rules in BR Switch (per-subscriber)
BR Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
2002::1
lw4over6 binding table
push IP-IP6 header (src=2002::1,dst=2001::1)
pop IP6 header
Forward to Internet
ACTION
MATCH
IPv4 traffic
IP-in-IPv6
dst_ip=1.2.3.4, dst_port&0xfc00=0x400
IP4-in-IP6 Packet
IPv4 Packet
Decapsulation Rule
Encapsulation Rule
ISP
Network
Internet
IPv4 Packet:
dst_ip=1.2.3.4 dst_port=1025
IP4-in-IP6 Packet:
dst_ip6=2001::1 src_ip6=2002::1
Rules Legend

## Slide 9: Example: lw4over6 3. CPE Forwarding Configuration
CPE Switch
2001::1
Customer Network
CPE Switch sends every initial packet of the same (source_ip, source_port) flow to controller
Controller allocates available public IPv4 address+port, and installs forwarding rules in CPE Switch (per-flow)
IPv4 Packet: src_ip=192.168.1.2 src_port=30000
Private IP | Private Port | Public IP | Public Port
192.168.1.2 | 30000 | 1.2.3.4 | 1025
NAT state table (for CPE 2001::1)
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
lw4over6 binding table
set dst_ip=192.168.1.2
set dst_port=30000
pop IP6 header
set src_ip=1.2.3.4
set src_port=1025
push IP-IP6 header (src=2001::1,dst=2002::1)
src_ip=192.168.1.2 src_port=30000
dst_ip=1.2.3.4 dst_port=1025
IP-in-IPv6
ACTION
MATCH
Controller
Encapsulation Rule
Decapsulation Rule
NAT Rule
ISP Network
IP4-in-IP6 Packet: dst_ip=1.2.3.4 dst_port=1025
IPv4 Packet: dst_ip=192.168.1.2 dst_port=30000
IP4-in-IP6 Packet:
src_ip6=2001::1 dst_ip6=2002::1 src_ip=1.2.3.4 src_port=1025
Rules Legend

## Slide 10: Example: lw4over6 4. Mesh Mode
Can easily support mesh mode: Change dst_ip of IPv6 tunneling action
Controller identifies dst_ip and dst_port of a flow:
  Another CPE : let dst_ip=IPv6 address of the CPE
  Otherwise: let dst_ip=BR address

## Slide 11: Status
Individual draft submitted to int-area WG: http://tools.ietf.org/html/draft-cui-intarea-unified-v6-framework-01
Presented in IETF89 Softwire WG meeting

## Slide 12: Backup: “Optimizing” NAT
Allow switches to have a dedicated NAT module
  Addresses configured by controller (possible through NETCONF)
  Co-operator with flow table: forward all flows to NAT virtual interface
  Do not need talking to controller per flow
Keep the ability of controller based NAT
  Switches could be asked to forward “important” flows to improve service quality
  In CPE side, easy to implement mesh mode of lw4over6 & MAP
Tradeoff: Flexibility V.S. Efficiency