## Slide 1: Unified IPv6 Transition Framework With Flow-based Forwarding
draft-cui-softwire-unified-v6-framework-00 (was draft-cui-intarea-unified-v6-framework-01)

## Slide 2: Motivation
There has been many softwire transition mechanisms
  Lightweight 4over6, MAP-E etc.
Difficulty on addressing / provisioning
  MAP: Algorithmic mapping between IPv4/IPv6 addressing
  Lw4over6: Needs dynamic binding between IPv4/IPv6 addresses
More flexible and cost effective by applying softwire defined networking

## Slide 3: Introduction
Design a unified framework for IPv6 transition
  Can cover current transition scenarios (Especially IPv4 over IPv6 tunneling)
  Reduce unnecessary configuration/operations in current mechanisms
Based on SDN
  Replace routers with OpenFlow switches
  Use centralized controller to define network behavior, and manage devices

## Slide 4: Architecture
CPE Switch
BR Switch
ISP IPv6 Network
Customer Network
Internet
Controller
OpenFlow Switch
Replace MAP CE, lwB4, …
As customer network gateway
OpenFlow Switch
Replace MAP BR, lwAFTR, …
  OpenFlow Controller
  Manage CPE/BR Switches: IP addressing, forwarding states, etc.
  May combined with traditional servers (e.g. DHCPv6 server)

## Slide 5: Switch Configuration
CPE configuration: Core function in softwire mechanisms
Device configuration
  Initially, each CPE Switch is configured with:
    An IPv6 address Connect to controller through IPv6
    Controller’s IPv6 address
  Automatic configuration for CPE Switch: through DHCPv6
Forwarding configuration
  Use Openflow for configuring Switches’ forwarding rules
  Configure on each flow
  Rule format: Match - Action
  Softwire information can be embedded into a rule, no provisioning needed
    E.g. BR Address – destination address parameter of CPE’s tunneling action IPv4 address and ports – conditions of BR’s matching rule, or value of set-field action (to implement NAT44)

## Slide 6: Requirements for Switches
On top of OpenFlow switch
Action:
  Support IPv6 tunneling action
Match:
  BR Switch: Support match field masking for ports (For MAP/lw4o6) => Let BR Switch treat all traffic from the same IPv4 address + port set as a single flow

## Slide 7: Example: lw4over6 1. CPE Device Configuration
CPE Switch requests an IPv6 address (or prefix), and builds OpenFlow connection
Controller allocates an IPv4 address + PSID for the CPE, and installs forwarding rules in BR Switch (per-subscriber) (Can also move to the first packet_in from the CPE)
CPE Switch
BR Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
allocate 2001::1 through DHCPv6
dst_ip=1.2.3.4, dst_port&0xfc00=0x400
2002::1
OpenFlow connection
lw4over6 binding table
push IP-IP6 header (src=2002::1,dst=2001::1)
install rule

## Slide 8: Example: lw4over6 1. CPE Device Configuration
CPE Switch requests an IPv6 address (or prefix), and builds OpenFlow connection
Controller allocates an available IPv4 address + PSID for the CPE in local binding table (Can also delay until the first packet_in from the CPE)
CPE Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
allocate 2001::1 through DHCPv6
OpenFlow connection
lw4over6 binding table

## Slide 9: Example: lw4over6 2. BR Forwarding Configuration
For every binding state: Controller installs forwarding rules in BR Switch (per-subscriber)
BR Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
dst_ip=1.2.3.4, dst_port&0xfc00=0x400
2002::1
lw4over6 binding table
push IP-IP6 header (src=2002::1,dst=2001::1)
IP-in-IPv6
pop IP-IP6 header; send back to the switch
src_ip=1.2.3.4, src_port&0xfc00=0x400
normal forward

## Slide 10: Example: lw4over6 3. CPE Forwarding Configuration
CPE Switch
Controller
2001::1
Customer Network
CPE Switch sends every initial packet of the same (source_ip, source_port) flow to controller
Controller allocates available public IPv4 address+port, and installs forwarding rules in CPE Switch (per-flow)
Packet: src_ip=192.168.1.2 src_port=30000
CPE | Private IP | Private Port | Public IP | Public Port
2001::1 | 192.168.1.2 | 30000 | 1.2.3.4 | 1025
CPE NAT state table
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
lw4over6 binding table
dst_ip=1.2.3.4 dst_port=1025
set dst_ip=192.168.1.2
set dst_port=30000
IP-in-IPv6
pop IP-IP6 header; send back to the switch
Unknown packet
Packet_in
src_ip=192.168.1.2 src_port=30000
set src_ip=1.2.3.4
set src_port=1025
push IP-IP6 header (src=2001::1,dst=2002::1)

## Slide 11: Status
Individual draft submitted to int-area WG: http://tools.ietf.org/html/draft-cui-intarea-unified-v6-framework-01
Presented in IETF89 Softwire WG meeting

## Slide 12: Backup: “Optimizing” NAT
Allow switches to have a dedicated NAT module
  Addresses configured by controller (possible through NETCONF)
  Co-operator with flow table: forward all flows to NAT virtual interface
  Do not need talking to controller per flow
Keep the ability of controller based NAT
  Switches could be asked to forward “important” flows to improve service quality
  In CPE side, easy to implement mesh mode of lw4over6 & MAP
Tradeoff: Flexibility V.S. Efficiency