## Slide 1: Unified IPv6 Transition Framework With Flow-based Forwarding
draft-cui-softwire-unified-v6-framework-00 Presenter: Cong Liu

## Slide 2: Motivation
There has been many softwire transition mechanisms
  Lightweight 4over6, MAP-E etc.
Difficulty on addressing / provisioning
  MAP: Algorithmic mapping between IPv4/IPv6 addressing
  Lw4over6: Needs dynamic binding between IPv4/IPv6 addresses
More flexible and cost effective by applying softwire defined networking
  Unify softwire provisioning
  Re-use same forwarding device for all mechanisms

## Slide 3: Introduction
Design a unified framework for IPv6 transition
  Support IPv4 over IPv6 tunneling scenario
  Reduce unnecessary configuration/operations in current mechanisms
Based on SDN
  Replace routers (CPE & BR) with OpenFlow switches
    Keep other devices in ISP network unchanged
  Use centralized controller to manage network behavior
CPE Switch
BR Switch
ISP IPv6 Network
Customer Network
Internet
Controller
OpenFlow Switch
Replace MAP CE, lwB4, …
As customer network gateway
OpenFlow Switch
Replace MAP BR, lwAFTR, …
  OpenFlow Controller
  Manage CPE/BR Switches: IP addressing, forwarding states, etc.

## Slide 4: Forwarding Configuration
Use Openflow for configuring Switches’ forwarding rules
Rule format: Match – Action
  Match conditions: specify a set of packets (as a flow)
  Actions: apply to all packets of the flow
Softwire information are embedded into forwarding rules, no DHCPv6-based provisioning needed
  BR Address: Destination address of CPE’s tunnel encapsulation action
  IPv4 address and PSID: Matching conditions of BR’s downstreaming rules, values of set-field actions (to implement NAT44)

## Slide 5: Device configuration
In order to connect to the controller, each Switch is configured with:
  An IPv6 address/prefix
  Controller’s IPv6 address, port, etc.
CPE Switches require automatic configuration
  Be compatible with RFC7084: Support DHCPv6 P
  Controller Information: DHCPv6 or NETCONF (?)

## Slide 6: Requirements for Switches
On top of OpenFlow switch
Action:
  Both CPE&BR: Support IPv6 tunneling encapsulation / decapsulation actions
Match:
  BR Switch: Support match field masking for ports (Reduce number of rules, BR Switch treat all traffic to the same IPv4 address + port set as a single flow)

## Slide 7: Example: 4over6
Controller preserves IPv4 addr+PSID for each CPE
  During CPE’s IPv6 provisioning
  MAP style: calculate from CPE’s IPv6 prefix
  Lw4o6 style: dynamic allocate
BR Switch provisioned with per-subscriber scale forwarding rules
  IPv6 tunneling encapsulation / decapsulation rule for each CPE
CPE Switch provisioned per-flow scale forwarding rules
  IPv6 tunneling encapsulation / decapsulation rule for all flows
  NAT rule for each flow (re-write IPv4 address and port)
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
lw4over6 binding table
CPE Switch
BR Switch
ISP IPv6 Network
Customer Network
Internet
Controller
Per-subscriber scale rules
Per-flow scale rules
2002::1
2001::1
Packet in

## Slide 8: Example: 4over6 BR Forwarding Configuration
For every binding entry: Controller installs forwarding rules in BR Switch (per-subscriber)
  Decapsulation Rule: upstream to Internet
  Encapsulation Rule: downstream to CPE
BR Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
2002::1
lw4over6 binding table
push IP-IP6 header (src=2002::1,dst=2001::1)
pop IP6 header
Forward to Internet
ACTION
MATCH
IPv4 traffic
IP-in-IPv6
dst_ip=1.2.3.4, dst_port&0xfc00=0x400
IP4-in-IP6 Packet
IPv4 Packet
Decapsulation Rule
Encapsulation Rule (per-subscriber)
ISP
Network
Internet
IPv4 Packet:
dst_ip=1.2.3.4 dst_port=1025
IP4-in-IP6 Packet:
dst_ip6=2001::1 src_ip6=2002::1
Rules Legend

## Slide 9: Example: 4over6 3. CPE Forwarding Configuration
CPE Switch
2001::1
Customer Network
CPE Switch sends every initial packet of the same (source_ip, source_port) flow to controller
Controller allocates available public IPv4 address+port, and installs forwarding rules in CPE Switch (per-flow)
IPv4 Packet: src_ip=192.168.1.2 src_port=30000
Private IP | Private Port | Public IP | Public Port
192.168.1.2 | 30000 | 1.2.3.4 | 1025
NAT state table (for CPE 2001::1)
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
lw4over6 binding table
set dst_ip=192.168.1.2
set dst_port=30000
pop IP6 header
set src_ip=1.2.3.4
set src_port=1025
push IP-IP6 header (src=2001::1,dst=2002::1)
src_ip=192.168.1.2 src_port=30000
dst_ip=1.2.3.4 dst_port=1025
IP-in-IPv6
ACTION
MATCH
Controller
Encapsulation Rule
Decapsulation Rule
NAT Rule
ISP Network
IP4-in-IP6 Packet: dst_ip=1.2.3.4 dst_port=1025
IPv4 Packet: dst_ip=192.168.1.2 dst_port=30000
IP4-in-IP6 Packet:
src_ip6=2001::1 dst_ip6=2002::1 src_ip=1.2.3.4 src_port=1025
Rules Legend

## Slide 10: Example: lw4over6 Mesh Mode
Can easily support mesh mode: On CPE, use per-flow level encapsulation rule
Controller checks the flow’s destination and set the dst_ip of the flow’s IPv6 tunnel encapsulation action
  Destined to another CPE : set dst_ip=the CPE’s IPv6 address
  Otherwise: let dst_ip=BR address

## Slide 11: Next Step
Comments?
Move forward in Softwire Workgroup?

## Slide 12: Backup: Optimizing NAT
Allow switches to have a dedicated NAT module
  External address configured by controller (possible through NETCONF)
  Co-operator with flow table: forward all flows to NAT virtual interface
  Do not need talking to controller per flow
Keep the ability of controller based NAT
  Switches could be asked to forward “important” flows to improve service quality
  In CPE side, easy to implement mesh mode of lw4over6 & MAP
Tradeoff: Flexibility V.S. Efficiency