## Slide 1: Unified IPv6 Transition Framework With Flow-based Forwarding
draft-cui-softwire-unified-v6-framework-00 Presenter: Cong Liu

## Slide 2: Motivation
There has been many softwire transition mechanisms
  Generally look the same, with differences on: addressing, provisioning, address sharing policy, etc.
This work is trying to discover a “unified” approach for softwire mechanism
  Use existing methods, currently based on openflow
  Unify softwire provisioning
  Unify forwarding devices

## Slide 3: Introduction
Mainly focus on IPv4 over IPv6 tunneling scenario
Replace routers (CPE & BR) with OpenFlow switches
  Keep other devices in ISP network unchanged
Centralized controller to manage provisioning & forwarding rule
CPE Switch
BR Switch
ISP IPv6 Network
Customer Network
Internet
Controller
OpenFlow Switch
Replace MAP CE, lwB4, …
As customer network gateway
OpenFlow Switch
Replace MAP BR, lwAFTR, …
  OpenFlow Controller
  Manage CPE/BR Switches: IP addressing, forwarding states, etc.

## Slide 4: Device configuration
Before connect to the controller, each switch is configured with:
  An IPv6 address/prefix
  Controller’s IPv6 address, port, etc.
CPE Switches require automatic configuration
  Be compatible with RFC7084: Support DHCPv6 PD
  Controller Information: DHCPv6 or NETCONF (?)

## Slide 5: Forwarding Configuration
Use Openflow-style forwarding rule for switches
  Rule format: Match – Action
Softwire information are represented by forwarding rules, do not need DHCPv6-based provisioning
  BR Address: Destination address of CPE’s tunnel encapsulation action
  IPv4 address and PSID: Matching conditions of BR’s downstreaming rules, values of set-field actions (to implement NAT44)

## Slide 6: Requirements for Switches
On top of OpenFlow switch
Action:
  Both CPE&BR: Support IPv6 tunneling encapsulation / decapsulation actions
Match:
  BR Switch: Support match field masking for ports (BR Switch can then treat all traffic to the same IPv4 address + port set as a single flow)

## Slide 7: Example: 4over6
Controller preserves IPv4 addr+PSID for each CPE
  MAP style: calculate from CPE’s IPv6 prefix
  Lw4o6 style: dynamic allocated
BR Switch forwarding rules:
  IPv6 tunneling encapsulation / decapsulation rule for each CPE
CPE Switch forwarding rules:
  IPv6 tunneling encapsulation / decapsulation rule for all flows
    Mesh mode: variable tunnel destination address for each destination
  NAT rule for each flow (re-write IPv4 address and port)
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
lw4over6 binding table
CPE Switch
BR Switch
ISP IPv6 Network
Customer Network
Internet
Controller
Per-subscriber scale rules
Per-flow scale rules
2002::1
2001::1
Packet in

## Slide 8: NAT Fallback
Allow switches to handle NAT locally
  Implemented by a virtual interface or iptables
  Needs automatically configuration for external address and ports
Keep the ability of controller based NAT
  Switch could handle “important” flows to improve service quality
Tradeoff: Flexibility V.S. Efficiency

## Slide 9: Next Step
Comments?
Move forward in Softwire Workgroup?

## Slide 10: Backup: 4over6 BR Forwarding Configuration
For every binding entry: Controller installs forwarding rules in BR Switch (per-subscriber)
  Decapsulation Rule: upstream to Internet
  Encapsulation Rule: downstream to CPE
BR Switch
Controller
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
2002::1
lw4over6 binding table
push IP-IP6 header (src=2002::1,dst=2001::1)
pop IP6 header
Forward to Internet
ACTION
MATCH
IPv4 traffic
IP-in-IPv6
dst_ip=1.2.3.4, dst_port&0xfc00=0x400
IP4-in-IP6 Packet
IPv4 Packet
Decapsulation Rule
Encapsulation Rule (per-subscriber)
ISP
Network
Internet
IPv4 Packet:
dst_ip=1.2.3.4 dst_port=1025
IP4-in-IP6 Packet:
dst_ip6=2001::1 src_ip6=2002::1
Rules Legend

## Slide 11: Backup: 4over6 CPE Forwarding Configuration
CPE Switch
2001::1
Customer Network
CPE Switch sends every initial packet of the same (source_ip, source_port) flow to controller
Controller allocates available public IPv4 address+port, and installs forwarding rules in CPE Switch (per-flow)
IPv4 Packet: src_ip=192.168.1.2 src_port=30000
Private IP | Private Port | Public IP | Public Port
192.168.1.2 | 30000 | 1.2.3.4 | 1025
NAT state table (for CPE 2001::1)
IPv4 addr | Port set | IPv6 addr
1.2.3.4 | 1024-2047 | 2001::1
lw4over6 binding table
set dst_ip=192.168.1.2
set dst_port=30000
pop IP6 header
set src_ip=1.2.3.4
set src_port=1025
push IP-IP6 header (src=2001::1,dst=2002::1)
src_ip=192.168.1.2 src_port=30000
dst_ip=1.2.3.4 dst_port=1025
IP-in-IPv6
ACTION
MATCH
Controller
Encapsulation Rule
Decapsulation Rule
NAT Rule
ISP Network
IP4-in-IP6 Packet: dst_ip=1.2.3.4 dst_port=1025
IPv4 Packet: dst_ip=192.168.1.2 dst_port=30000
IP4-in-IP6 Packet:
src_ip6=2001::1 dst_ip6=2002::1 src_ip=1.2.3.4 src_port=1025
Rules Legend