## Slide 1: Unified IPv6 Transition Framework With Flow-based Forwarding
draft-cui-softwire-unified-v6-framework-00 (was draft-cui-intarea-unified-v6-framework-01)

## Slide 2: Motivation
There has been many IPv6 transition mechanisms
  Softwire: DS-Lite, Lightweight 4over6, MAP-E etc.
Each has disadvantages
  MAP: Algorithmic mapping between IPv4/IPv6 addressing
  Lw4over6: Needs dynamic binding between IPv4/IPv6 addresses
More flexible and cost effective if we can design a unified framework

## Slide 3: Introduction
Design a unified framework for IPv6 transition
  Can cover current transition scenarios (especially IPv4 over IPv6 tunneling)
  Reduce unnecessary configuration/operations in current mechanisms
Based on SDN: Flow-based Forwarding, Separate control plane and data plane
  Replace routers with OpenFlow switches
  Centralized controller to define network behavior, and manage devices

## Slide 4: Solution Architecture
CPE/BR Switches
  Deployed at the border of network
  Perform flow-based forwarding function
    Support actions: forwarding, tunneling, IP translation, etc.
Controller
  Manage IPv4/IPv6 addressing
  Configure switches’ flow tables

## Slide 5: CPE Configuration
Forwarding configuration: OpenFlow
  Configure on each flow
  Specify forwarding rules to each flow
  Softwire addresses can be embedded into a rule
Device configuration: Through DHCP/NETCONF
  Configure on startup
  Including IPv6 address, Prefix delegation, interface configuration, NAT configuration, etc.
  Should be limited to only necessary information that can not be configured by OpenFlow
    Can be embed into forwarding rules: BR (tunnel) address, IPv4 internal address, …
DHCPv6-based softwire option provisioning: NOT USED

## Slide 6: Requirements for Switches
(On top of OpenFlow switch)
Actions:
  IPv6 tunneling (For tunneling mechanism)
  IPv4/IPv6 translation (For translation mechanism)
Match:
  Support match field masking for ports (For MAP/lw4o6, on BR Switch) => lwAFTR treat all traffic of the same IPv4 addr+PSID as a single flow

## Slide 7: Example: 4over6
2001::1/64
192.168.0.1/24
Maintaining per-subscriber state
IPv4 addr | Port set | IPv6 addr
58.205.200.1 | 1024-2047 | 2001::1
Forwarding rule
v4-in-v6 packet
v4 packet
v4 packet
②
③
④
④
⑤
⑥
①
Pre-configuration: IPv6 PD, etc.
Flow on CPE’s IPv4 address and port set
Flow on 5-tuple or source IP, according to NAT policy
Masking based match for port

## Slide 8: NAT issue
Allow switches to have a dedicated NAT module
  Addresses configured by controller (possible through NETCONF)
  Co-operator with flow table: forward all flows to NAT virtual interface
  Do not need talking to controller per flow
Keep the ability of controller based NAT
  Switches could be asked to forward “important” flows to improve service quality
  In CPE side, easy to implement mesh mode of lw4over6 & MAP
  Tradeoff: Flexibility V.S. Efficiency

## Slide 9: Status
Individual draft submitted to int-area WG: http://tools.ietf.org/html/draft-cui-intarea-unified-v6-framework-01
Presented in IETF89 Softwire WG meeting
Will re-submit to softwire WG (mainly solving NAT issues)

## Slide 10
Thanks!